## Slide 1: IRIS workshop Ranger and Adrestea
Narasinga Rao Miniskar, Aaron Young, Anthony Cabrera, Frank Liu, Jeffrey Vetter
Architecture & Performance Group
04-Jan-2022
ORNL is managed by UT-Battelle for the US Department of Energy
https://csmd.ornl.gov/profile/narasinga-rao-miniskar miniskarnr@ornl.gov

## Slide 2: RANGER PLATFORM

## Slide 3: About RANGER
Future of HPC: Heterogenous Computing
Proposal
  RANGER Platform: Hardware assisted task scheduling framework
  RISC-V cores with Accelerators
  Extended GEM5 simulator for RANGER platform
  Hierarchical Task Scheduler (TS)
    Local level: Task into fine grained sub-tasks ; Accelerator Specific TS
    Global level: Coarse grain task specification with programming portability; Coarse grain TS
Task Scheduling Challenges
  Balance application performance and programmability
  Varying data communication time between tasks
  Varying computation time across different variants of accelerators

## Slide 4: State of the art for Heterogenous Task Schedulers
Popular Static Task Scheduler: PEFT (Predict Earliest Finish Time)
  Considers impact of current scheduling decision on subsequent decisions
Task: Atomic unit for data transfer and computation
  Can be portioned into finer sub-tasks
  Smaller fine grain sub-tasks (streaming)
    Lesser scratch pad memory
    More scheduling opportunity but increases complexity
    Less efficient (Reasonable) data transfers due to large number of sub-tasks
    Accelerator friendly
    Data transfers overlaps with computation
Task | T1 | T2 | T3 | T4 | T5 | T6 | T7 | T8 | T9 | T10
P1 | 22 | 22 | 32 | 7 | 29 | 26 | 14 | 29 | 15 | 13
P2 | 21 | 18 | 27 | 10 | 27 | 17 | 25 | 23 | 21 | 16
P3 | 36 | 18 | 43 | 4 | 35 | 24 | 30 | 36 | 8 | 33
T1
T2
T3
T4
T5
T6
T7
T8
T9
T8
17
31
29
13
7
7
7
16
11
57
5
9
42
3
30
CCM* for each task on 3 devices
* CCM: Cost Computation Matrix

## Slide 5: Vanilla Platform with Heterogenous Accelerators
Centralized Heterogenous Scheduler: PEFT
Complexity depends on the number of tasks
Accelerators and DMAs are controlled by Host
Needs bigger local memories (scratchpads)
Host (RISC-V)
Run-time Framework
Task graph submission
Application
Derive Task Graph
FIFO
Interconnect : Shared Bus / NoC
Centralized
Heterogenous Scheduler
Task Dispatch
Application
Application
FIFO
Task Metadata Initialization
Main
Memory
(DDR4 / HBM)
DMAs
DMAs
DMAs
Accelerator-2
(Conv128)
Accelerator-1
(Conv1024)
Accelerator-N
(Dense)
FIFO
FIFO
Scheduler
H2D
D2H
K1
(kernel)
H2D
D2H
K1
(kernel)
K2
(kernel)
K3
(kernel)
Convolution
BN
Pooling
Conv
K4
(kernel)
K5
(kernel)
K6
(kernel)
BN
Pooling
Conv
Convolution Streamed Tasks (Tiles)
~10000s Tasks

## Slide 6: RANGER Platform with Heterogenous Accelerators
Accelerator Interface: Memory-mapped IO
RISC-V for host and accelerator devices
GEM5 based modeling and simulation
Perfect for stream dataflow tasks
Host (RISC-V)
IRIS Run-time Framework
Task graph submission
Application
Derive Task Graph
FIFO
Interconnect: Shared Bus (AXI4)/NoC
Coarse grain
Scheduling Policy
(PEFT)
Task Dispatch
Application
Application
FIFO
Task Metadata Initialization
Hierarchical Scheduler
Device-1(RISC-V)
Device-2(RISC-V)
Main
Memory
( DDR4 /
HBM /
3D-Memory )
DMAs
DMAs
DMAs
Accelerator-2
(Conv128)
Task Interface
ASCS
Accelerator-1
(Conv1024)
Task Interface
Fine grain:
ASCS
Device-N(RISC-V)
Accelerator-N
(Dense)
Task Interface
ASCS
FIFO
FIFO
Accelerator
MEMCTRL
DMA
In
SRAM (Buffers)
DMA
Out
RISC-V (ASCS Scheduler)
Ctrl
Memory Mapped IO
Device
Wide bus
Data
Ctrl
Data
Ctrl

## Slide 7: Hierarchical Task Scheduler Flow (ISC-Paper)
OpenCL supports data flow pipelines
  Use cases: FPGA, GPU
  Needs support in IRIS (TBD)
For custom accelerators
  Accelerator specific command scheduler
Why Accelerator Specific?
  Configurable Tile size
  Configurable Data reuse
  Synchronize DMAs and Accelerators
  Programmable is a best solution
  Generic solution is possible, but cannot satisfy timing constraints
    Hardware task scheduler solution can be an option
Heterogenous device Scheduler
(PEFT)
Task Graph
With profile data
Scheduler (RISC-V)
Host (RISC-V)
Device (RISC-V)
T1
DMAIN
Kernel
DMAOut
T1
T2
Accelerator specific
Stream Command Scheduler
(ASCS)
DMA IN-1
Task with
Commands
Kernel-1
DMA Out-1
To DMAIn
To Accelerator
To DMAOut
Sub-tasks
1st Level
Coarse Grain Scheduler
2nd Level
Fine Grain Scheduler
15
T1
T2
T3
T4
T5
T6
10
10
8
12
12
DMA-In-1
Kernel-1
DMA-Out-1
T0
T1
T2
DMA-In-2
Kernel-2
DMA-Out-2
DMA-In-3
Kernel-3
DMA-Out-3
DMA-In-4
Kernel-4
DMA-Out-4
T3
T4
T5
Sub-Tasks Set-1
Sub-Tasks Set-2
Sub-Tasks Set-3
Sub-Tasks Set-4
Steady
State
L
C1
C2
C3
C4
L: Task initialization time
Ci: Configuration of DMAs & Accelerator

## Slide 8: Experimental Setup
List of kernel accelerators and their area estimations in a TSMC 16nm technology
Various heterogeneous designs, the number of kernel accelerators, and
the estimated area. Design A and B are the aliases of Design 1 and 2, respectively.
Inception-V3 DAG
IRIS-NN Task Graph + Host Code Generator (Python)
Run on
RANGER Platform
(GEM5 Simulator)
RISC-V
Build
Resnet, VGG
MobileNet, UNet
Inception-v3
Accelerators: Convolution (CONV), Batch Normalization (BN), Dense

## Slide 9: Experimental Evaluation: Makespan
Comparison of makespans for various RANGER and baseline designs. On average, RANGER achieves a 12.7×speedup
Baseline: Vanilla architecture with flattened stream tasks for centralized scheduler

## Slide 10: RANGER Speedup (Fixed 10 parallel instances of each application)
Measured speedup of RANGER by running 10 parallel instances of each application with respect to Designs 1–10, which contain an increasing number of kernel accelerators. The speedup plateaus at Design 3 due to an insufficient number of tasks for the available kernel accelerators
Inception-V3 DAG
10 instances

## Slide 11: RANGER Speedup (Increasing number of application instances)
Measured speedup of RANGER by running an increasing number of instances of the same application on Designs A–H.
RANGER demonstrates excellent scalability with 100 instances of application running in parallel
4 to 100 instances

## Slide 12: Area and Makespan Compared to Reference
Comparison of makespans for RANGER and reference. On average, RANGER shows only 10.88% of penalty,
which is the measurement of performance overhead of the local ASCS.
Reference: (Hypothetical) Identical number of Accelerators as its RANGER counterpart, but has huge scratchpad memory
Has large scratchpad to hold complete task I/O
Requires no local task scheduler

## Slide 13: RANGER Summary
Presents RANGER framework (Extremely heterogenous computing)
  An architecture design for hierarchical task scheduling
Hierarchical Task Scheduling
  Requires coarse grained task dependency specification
  Fine grain accelerator specific scheduling at lower level
RANGER uses customized RISC-V cores
Achieves 12.7x performance gain in terms of makespan
Area Overhead: +2.7% in a 16nm technology
Future work:
  Experiment different scheduling policies with HUNTER and DAGGER
  Hardware task scheduler

## Slide 14: Adrestea: An efficient FPGA design environment for scientific machine learning

## Slide 15: Why Adrestea and What is it?
FPGA Programming Challenges
  Writing interface program to communicate with FPGA kernels
  Writing kernels along with other heterogenous compute units
  Design space exploration
Adrestea: An efficient FPGA design environment for scientific machine learning applications to run at the edge
  Simplified call to FPGA kernel; Extended IRIS Runtime Framework (https://iris-programming.com)
  Enables to write kernel targeting other compute units as well with run-time selection
  An intelligent design space exploration environment for FPGAs
  Proof of concept:
    Application: Random forest classifier ; FPGA: Xilinx Alveo U250
SC 2022 Demo: https://ornl.sharepoint.com/:v:/s/CSMDSTAFF-ACSR-APG/EYN-bqYLgB5Msg_pd0oZJnUBbBTp-bkE4ba_K1CflpeGrA?e=jahFX0

## Slide 16: Automated Adrastea Development Environment
1) Build Hardware Designs
Automated Builds
2) Run Hardware Designs
Automated Runs
Heterogeneous Hardware Accelerators
Hardware
Optimization
Loop
Vitis Build Server
GitLab-CI
Slurm
FPGA
GPU
Vitis Run Server
GitLab-CI
Slurm
Bitfiles
Runtime
Results
Note: Servers are VMs with the Vitis toolchain installed and hardware added
with PCIe Passthrough.
This enables:
Easy configuration of development environment.
Easy migration of VMs to new hosts for additional resources.

## Slide 17: Application: Random Forest (RF) Classifier With IRIS
1
2
3
4
5
Tree-1 Class
f1 < 0.4
f2 < 0.2
f3 < 0.1
f5 < 0.1
f4 < 12.5
a
b
1
2
3
4
5
Tree-N Class
f3 < 0.1
f1 < 0.5
f2 < 0.5
f4 < 10.0
f5 < 0.5
Decision Tree Classification
Voting (Histogram)
Majority Voting (Class with maximum votes)
Random Forest Xilinx Generator Script
RF Models
XilinxCL Kernel

## Slide 18: Application build with IRIS
Host Code
kernel.cl
Kernel.xilinx.cpp
kernel.cpu.cpp
CPU call
FPGA (OpenCL/XilinxCL),
CPU, GPU task specification
$ export XCL_EMULATION_MODE=sw_emu
$ cmake –DUSE_XILINX=ON ../
$ make –j install
$ cd install
$ ./irf 3 # RUN on FPGA
Build Commands
CMakeLists.txt

## Slide 19: BRISBANE Macros and Interface Code Generation
IRIS Task Calls Extractor And
Kernel Interface Generator (Python)
Interface code for OpenMP/Hexagon kernels:
brisbane_rf_classifier_setarg
brisbane_rf_classifier_setmem
brisbane_setarg
brisbane_setmem
brisbane_kernel
brisbane_launch
Notes: #IN_BRISBANE(IRIS_VARIABLE, Type, Element Type, HOST_VARIABLE, SIZE, Compute_Constraints)
#OUT_BRISBANE(IRIS_VARIABLE, Type, Element Type, HOST_VARIABLE, SIZE, Compute_Constraints)
#PARAM(VARIABLE_NAME, Type, Compute_Constraints)

## Slide 20: RF Xilinx Generator Knobs and Optimizations
Algorithmic Knobs
  Fixed point knobs
  Data type (8-bit, 16-bit, 32-bit)
  Bitwise optimizations
  Data layout optimizations
  Features pruning
  Voting arithmetic fusion
  Static single assignment of Voting
  Early prediction with confidence
  Configurable number of M-AXI interfaces and bitwidth
  Streaming tasks
Build knobs
  Clock Frequency
Compiler pragmas
  #pragma HLS PIPELINE II
  #pragma HLS INTERFACE axis port=classify_stream
  #pragma HLS INTERFACE m_axi port=batch_g0 bundle=maxiport0 offset=slave
  #pragma HLS INTERFACE ap_ctrl_none port=return
  #pragma HLS DATAFLOW
  #pragma HLS array_partition variable=
  #pragma HLS inline
  #pragma HLS unroll

## Slide 21
Sequential and Parallel threads with Streams
Sampling techniques: Random, DOEPY sampling techniques: Fractional factorial, Plackett Burman, Sukharev Grid, Box-Wilson, Latin hyper cube (LHC), Space filling LHC, Random K-mean cluster, Maximin, Halton, Uniform random matrix, DEFFE-Smart, DEFFE-One-dimension (Onedim)
ML: Keras/PyTorch-DNN, Random Forest, SVM
Evaluate: Multi-Thread, Slurm
Automated Design Space Exploration
S: Sampling (Indexes)
PV: Parameter Values
PN: Parameter Normalized Values
EO: Evaluation Output
BOE: Batch Output of Extraction (Cost metrics)
BOI: Batch Output of Inference (Cost metrics)
Sampling
Extract Parameters
Build
Run & Extract
ML Training
Write
S
S, PV, PN
BOE
S, PV, PN, BOE
BOI
0_single.py
validate.py
DEFFE
Config.json
Knobs, Costs and Explorations
S, PV, PN, EO
ML Inference
S, PV, PN
BOI
: Stream Queue
: Function Call
Extract Parameters
S
0_single.py
DEFFE: https://github.com/miniskar/deffe/tree/release.v1
[Miniskar et.al. CF2021]
(evaluate)
(extract)
1
2
3
1
2
3
4
1
2
1
2
3
4
5
# M-axis
1: 1
2: 2
3: 4
Fixed Point
Threshold
1: 100%
2: 90%
3: 80%
4: 70%
Bitwise
Optimizations
1: Yes
2: No
Frequency
1:50MHz
2: 100MHz
3: 200MHz
4: 300MHz
5: 500MHz
Onedim
Base
Knobs

## Slide 22: Single Run Script
Test Dataset
Input
Generator
Automated
FPGA Build
Output
Design Space Parameters
Automated Run and Collect Cost Metrics
Cost Metrics
RF Model
Build
Run and
Extract
FPGA Design
HLS Design
Single.py
Analyze.ipynb
DEFFE

## Slide 23: Analyze Jupyter Notebook
Cost Metrics

## Slide 24
Thank you

## Slide 25
IRIS-NN Task Graph + Host Code Generator (Python)
Run on
RANGER Platform
(GEM5 Simulator)
RISC-V
Build
Resnet, VGG
MobileNet
Inception-v3